## Slide 1: Transport Layer in WSN

## Slide 2: Main Objectives and Challenges
Objectives:
  Congestion control
  Reliable transport
  (De)multiplexing
Challenges
  End-to-End Measures
  Application-Dependent Operation
  Energy Consumption
  Biased Implementation
  Constrained Routing/Addressing

## Slide 3: End-to-End Measures
Traditional TCP
  Adopts end-to-end retransmission-based error control and window-based additive-increase multiplicative-decrease (AIMD) congestion control mechanisms.
  Provides end-to-end and point-to-point reliability and congestion control solutions.
  Packet losses and congestion mitigation are performed through communication between a source and a destination without any involvement from the intermediate parties.
  Reside only on the source and destination.
  Each ﬂow is considered independently to provide a point-to-point communication solution.
TCP for WSN
  End-to-end control mechanisms leads to resource wastage in WSNs, where collective information from a group of sensors is much more important than the individual information from each sensor node.
  If local measures for reliability and congestion control are employed it can improve the energy efﬁciency of the transport layer protocols.
  Reliability of the collective information from a group of sensors is controlled instead of the reliability of information from each individual sensor node.

## Slide 4: Application-Dependent Operation
Operation of WSNs are for a speciﬁc sensing application objective.
For a monitoring application reliability is the most important metric
For event detection applications timeliness is crucial.
Focus of the transport layer solutions should be tailored to the application.
The application can be developed for a wide range of purposes in the military, environment, health, space exploration, and disaster relief areas.
The importance of these metrics also varies according to the application area.
Objective of WSNs inﬂuences the design requirements of the transport layer protocols.

## Slide 5: Energy Consumption
Transport layer functionalities should be energy aware, i.e., the error and congestion control objectives must be achieved with the minimum possible energy expenditure.
If reliability levels at the sink are found to be in excess of that required for event detection, the source nodes can conserve energy by reducing the amount of information sent out or temporarily powering down.
End-to-end measures used for conventional networking for reliability, requires signiﬁcant energy consumption in a multi-hop network. These solutions are not be scalable for WSNs.
Transport layer protocol can be designed such that the reliability level can be traded off for decreased energy consumption through local reliability measures.

## Slide 6: Biased Implementation
Most of the functionalities should be performed at the sink with minimum functionalities required at the sensor nodes to conserve limited sensor resources and shifts the burden to the high-powered sink.
Moreover, the trafﬁc in the WSNs exhibits signiﬁcantly different characteristics depending on the ﬂow direction.
While the ﬂow in the sensors-to-sink direction may require timely delivery with loss-tolerant operation, the sink-to-sensors direction usually requires a high delivery ratio.
Transport protocols should be designed also by considering these biases in trafﬁc.

## Slide 7: Constrained Routing/Addressing
The design of transport layer protocols for WSNs should not assume the existence of an end-to-end global addressing
It may have attribute-based naming and data-centric routing, which call for different transport layer approaches.

## Slide 8: Transport Protocols for WSN
Reliable Multi-Segment Transport (RMST)
Pump Slowly, Fetch Quickly (PSFQ)
Congestion Detection and Avoidance (CODA)
Event-to-Sink Reliability (ESRT),
GARUDA and
Real-Time and Reliable Transport (RT)2

## Slide 9: Reliable Multi-Segment Transport (RMST) Protocol
End-to-end data-packet transfer reliability
  Each RMST node caches the packets
  When a packet is not received before the WATCHDOG timer expires, a NACK is sent backward
  The first RMST node that has the required packet along the path retransmits the packet
  In-network caching brings significant overhead in terms of power and processing
  Relies on Directed Diffusion
Placement of reliability for data transport at different layers of the protocol stack
  MAC layer
  Transport layer
  Application layer
  Combinations of above
Trade-off between implementation on the MAC vs Transport layer

## Slide 10: RMST
Implemented as a filter for Directed Diffusion
Takes advantage of Directed Diffusion for
  Routing
  Path recovery and repair
Adds to Directed Diffusion
  Fragmentation/reassembly management
  Guaranteed delivery
Receivers responsible for fragment retransmissions
  Receivers are not necessarily end points
  Caching or non-caching mode determines classification of node
Two types of loss detected by a “receiver”
  A “hole” in a sequence of fragments
  A truncated sequence
RMST considers 3 layers
  MAC
  Transport
  Application

## Slide 11: Error Recovery in non-caching mode

## Slide 12: Error Recovery in caching mode

## Slide 13: RMST
MAC Layer Choices
  No ARQ
    All transmissions are broadcast
    No RTS/CTS or ACK
    Reliability deferred to upper layers
    Benefits: no control overhead, no erroneous path selection
  ARQ always
    All transmissions are unicast
    RTS/CTS and ACKs used
    One-to-many communication done via multiple unicasts
    Benefits: packets traveling on established paths have high probability of delivery
  Selective ARQ
    Use broadcast for one-to-many and unicast for one-to-one
    Data and control packets traveling on established paths are unicast
    Route discovery uses broadcast

## Slide 14: RMST
Transport Layer Choices
  End-to-End Selective Request NACK
    Loss detection happens only at sinks (endpoints)
    Repair requests travel on reverse (multi-hop) path from sinks to sources
  Hop-by-Hop Selective Request NACK
    Each node along the path caches data
    Loss detection happens at each node along the path
    Repair requests sent to immediate neighbors
    If data is not found in the caches, NACKs are forwarded to next hop towards source
Application Layer Choices
  End-to-End Positive ACK
    Sink requests a large data entity
    Source fragments data
    Sink keeps sending interests until all fragments have been received
    Used only as a baseline

## Slide 15: RMST
NACKs triggered by
  Sequence number gaps
    Watchdog timer inspects fragment map periodically for holes that have aged for too long
  Transmission timeouts
    “Lost fragment” problem
NACKs propagate from sinks to sources
  Unicast transmission
  NACK is forwarded only if segment not found in local cache
  Back-channel required to deliver NACKs to upstream neighbors

## Slide 16: Qualitative Evaluation of RMST
Benefits
  In caching mode, RMST essentially creates reliable segments between two consecutive caching nodes and the retransmissions are performed inside these segments instead of through the end-to-end route.
  As a result, the cost associated with end-to-end retransmissions is minimized. Moreover, RMST aims to provide guaranteed delivery for each ﬂow in the WSN.
  This is helpful for applications where individual node information is important, such as in network management solutions.
Drawbacks
  May incur additional overhead since caching requires additional processing and memory at the caching nodes. This may increase the overall complexity and energy consumption of the network.
  Most applications may not require 100% reliability
  RMST treats each ﬂow separately, which may lead to overutilization of the resources in WSNs.
  Guaranteed reliability via in-network caching may bring signiﬁcant overhead for WSNs with power and processing limitations.
  Focuses only on the reliability aspects of communication. Since a packet-by-packet reliability notion is followed, a large amount of information may ﬂow inside the network. This will result in congestion and associated packet drops, which is not addressed in RMST.

## Slide 17: Pump Slowly, Fetch Quickly (PSFQ)
Address the path from sink to sensors
Pace the data from a source node at a relatively low speed to allow intermediate nodes to fetch missing data segments from their neighbors
  Assumption: no congestion, losses due only to poor link quality
Hop-by-hop recovery
Goals
  Recover from losses locally
  Ensure data delivery with minimum support from transport infrastructure
  Minimize signaling overhead for detection/recovery operations
  Operate correctly in poor link quality environments
  Provide loose delay bounds for data delivery to all intended receivers

## Slide 18: PSFQ
Three basic operations
  Pump: Slow pumping  Each node on the route to the destinations waits for a speciﬁc amount of time before relaying the messages.
  Fetch: In case of packet errors, each node performs aggressive hop-by-hop recovery to fetch the lost packets from neighbor nodes.
  Status reporting: Provides a reporting functionality that creates closed-loop communication between sensors and sink. Through this functionality, the sink can collect information related to operation of the network.
Alternate between multi-hop forwarding when low error rates and store-and-forward when error rates are higher

## Slide 22: Report Operation
Used to provide feedback data of delivery status to source nodes
  To minimize the number of messages, a report message travels back from a destination node to the source nodes
Intermediate nodes can piggyback their report messages in an aggregated manner
If report message is not received within Treport time the node generates its report and send it to the sink

## Slide 23: Qualitative Evaluation
Lightweight and energy efficient
Simple mechanism
Scalable and robust
Need to be tested for high bandwidth applications
Cache size limitation
Does not address congestion control

## Slide 24: Congestion Detection and Avoidance (CODA)
Aim  To detect and avoid congestion in WSNs
Three main congestion scenarios
  For traffic generation from source node, congestion builds up close to the source nodes because of the contention in the wireless channel  local congestion control mechanisms
  For low-rate trafﬁc, congestion can occur temporarily in hot spots, where multiple ﬂows are served  local congestion control mechanisms
  For traffic from persistent hot spots requires end-to-end mechanisms to regulate the data rate of source nodes.
Congestion Control Mechanisms
  Receiver-based congestion detection
  Open-loop hop-by-hop backpressure signaling to inform the source about the congestion,
  Closed-loop multi-source regulation for persistent and larger scale congestion conditions.

## Slide 25: CODA
Congestion Detection Metric
  Receiver based congestion detection mechanism
    Buffer occupancy level
      If the unused buffer level drops below a threshold level
    Channel Load Condition
      if the channel load is higher than a fraction of the maximum channel utilization

## Slide 26: Open-loop hop-by-hop back pressure
When a sensor node is trying to transmit a packet to the sink through a congested area and when the congestion is detected by one of the nodes inside the congested area the receiver broadcasts a suppression message toward the source node in the reverse path.
The suppression message is used to inform the upstream nodes about congestion.
Upon receiving the suppression, the upstream nodes decrease their sending rates or drop packets to relieve the congestion in the forward path.
The suppression message is rebroadcast until a non-congested node receives the message
The suppression message may not reach all the way to the source nodes, they serve to relieve local congestion in a hot spot area.
By using cross-layer routing techniques the forward path can be rerouted to avoid these hot spots.

## Slide 27: Open-loop hop-by-hop back pressure

## Slide 29: Closed loop multi-source regulation
The trafﬁc generated by the source nodes can create network-wide congestion.
If a source node injects a trafﬁc load larger than the network can handle, the local congestion control mechanism cannot relieve the congestion.
Similar to conventional end-to-end congestion control mechanisms.
If the source rate exceeds a threshold, r >= νSmax the source node enters closed-loop control.
A regulation bit is set in the header of the packets to inform the sink.
The sink begins sending periodic ACK messages for each n number of packets received.
If the source cannot receive the ACK messages, it determines network-wide congestion and decreases its source rate.
Smax  maximum theoretical throughput of the channel

## Slide 30: Closed loop multi-source regulation

## Slide 31: Qualitative Evaluation
Advantages
  Congestion is predicted more precisely by using a combination of buffer occupancy level and channel load condition
  Addresses both local and end-to-end congestion and hence a complete congestion control mechanism is provided for downstream trafﬁc.
  It can increase the network performance by avoiding congestion.
Disadvantages
  Does not address end-to-end transport reliability
  Closed-loop multi-source regulation mechanism incurs additional latency for cases where the network trafﬁc is high.

## Slide 32: Event-to-Sink Reliable Transport (ESRT) Protocol
Based on the event-to-sink reliability notion and provides reliable event detection without any intermediate caching requirements.
Address both the reliability and congestion problems
Main characteristic of information delivery in WSN
  Data-centric
  Collective information from multiple sensors regarding an event is much more important than the individual information sent from each node.
  Not a source to a destination flow, but an event-to-sink information ﬂow
Algorithms run mainly on the sink, with minimal functionality required at resource-constrained sensor nodes.
Relies on the sink to measure the reliability in the WSN every t time units, i.e. decision interval.

## Slide 33: ESRT
Reliability is measured in terms of the number of data packets from all the sensor nodes associated with an event.
Observed event reliability, ri , is the number of received data packets in decision interval i at the sink.
Desired event reliability, Ri, is the number of data packets required for reliable event detection. This is determined by the application.
Conﬁgures the reporting rate, f, of source nodes so as to achieve the required event detection reliability, R, at the sink with minimum resource utilization.

## Slide 35
To control congestion in the network, the sink needs to determine the operating region of the network.
This operating region depends on two factors: whether congestion exists in the network and whether the required reliability is achieved.
Two mechanisms are required to estimate the congestion and the reliability state of the network.
In each decision interval, t, the sink determines whether the network is operating in the low- or high-reliability region according to the number of packets received in that interval.
A congestion detection algorithm is employed at each sensor node in the network.
The sink determines the operating region of the network.
According to the operating region, the sink controls the reporting rate of the sensor nodes to operate at the optimal operating region (OOR).

## Slide 36
For congestion detection
  Each sensor node monitors the local buffer-level
  The increment in the buffer fullness level at the end of each reporting interval is expected to be constant.
  bk = buffer fullness level at the end of kth reporting level
  bk-1 = buffer fullness level at the end of (k-1)th reporting level
  b = bk - bk-1
  B = Buffer size
  If bk + b > B  congestion in the next reporting interval.
  If a sensor node detects congestion in the network, it notiﬁes the sink by piggybacking the packets that are sent.
  The state of the network is determined at each decision interval through the reliability measurement and congestion notiﬁcations.
  The sink updates the reporting rates of the sensor nodes by broadcasting a packet to each sensor node.
  fi = reporting rate in decision interval i
  i = reliability level in decision interval i

## Slide 37: Reporting Rate Decision
Network Operating Region | Reporting Rate fi+1
NC, LR | 
NC, HR | 
C, HR | 
C, LR | 
OOR | 
Network Operating Region | Reporting Rate fi+1
NC, LR | 
NC, HR | 
C, HR | 
C, LR | 
OOR | 

## Slide 38: Qualitative Evaluation
Advantages
  Introduces a novel reliability notion event-to-sink reliability.
  Efﬁcient congestion control and reliability mechanisms are provided by shifting the decision mechanism to the power-rich sink node.
  Achieves both reliability and conserving energy.
  The required reliability is achieved with minimum energy consumption and without network congestion.
  Through distributed update mechanisms, ESRT converges to the optimum operating state regardless of the initial network state.

## Slide 39
Disadvantages
  It relies on the assumption that the base station is one hop away from all the sensor nodes, i.e., a sink broadcast for frequency update will be received by all sensor nodes. Although this assumption may hold true for a certain class of application, as the network size increases, multi-hop strategies are required for information delivery from the sink to the sensors.
  ESRT maintains the same value of operating frequency, f , at the end of each decision interval for each sensor node. In case a large group of sensors sense an event, the required operating frequency may not be the same for all these sensors because of their local interactions in the network.
  The event-to-sink reliability notion applies to cases where the information at each sensor is correlated.
  It cannot be applied for applications where individual sensor information is necessary.

## Slide 40: Real Time Reliable Transport (RT2)Protocol
Reliably and collaboratively transport event features from the sensor field with minimum energy dissipation in a timely manner
Addresses both congestion control and reliability
First protocol to focus on real-time guarantees
Challenges
  Timely delivery  Delay based reliability
  Channel errors and node failures  Packet level reliability mechanism at Transport Layer
  Energy Efficiency  Energy aware protocol

## Slide 41: (RT2)Protocol
Follows collective event transport reliability as in ESRT
Event delay bound  To meet application specific deadlines
Definitions
  Observed delay-constrained Event Reliability (DRi) No. of packets received with a certain delay bound at the sink in a decision interval i.
  Desired delay-constrained Event Reliability (DR*)  Min. no. of packets required for reliable event detection within a certain application specific delay bound.
  Delay-constrained Reliability Indicator (i) DRi/DR*

## Slide 42
For each decision interval i, the sink observes DRi
DRi > DR*  Event is reliably detected within delay bound
Otherwise adjust reporting rate f
RT2
  To configure the reporting rate, f, of source nodes so as to achieve the required event detection reliability, DR*, at the actor node within the application-specific delay bound
Delay-constrained reliability - e2a
  Event Transport Delay (tran) – Overall time between the event occurrence time and the time when the event is reliably transported to the sink.
    Buffering delay
    Channel access delay
    Propagation delay
  Event Processing Delay (proc) – Processing delay experienced at the sink when the desired features of the event are estimated using the data packets received from the sensor field. Includes the duration of wait to receive adequate samples from the sensor nodes.
  Action delay (act) – Time taken from the instant when an event is reliably detected at the sink to the instant when a particular action is performed
e2a >= tran + proc + act

## Slide 43
tran depends on network load and congestion level
Network load depends on event reporting frequency f
End-to-end delay depends on queuing delay ar each relay node
RT2 employs a Time-Critical Event First scheduling (TCEF) policy
  Elapsed time is piggybacked in packet by each node
  The packet with shortest remaining time is scheduled first
Updates the reporting frequency to mitigate congestion

## Slide 44: Effect of reporting frequency on On-time delivery
N – No. of Sources

## Slide 45: Effect of reporting frequency on Reliability

## Slide 46
Delay-constrained event reliability depends on congestion and congestion depends on reporting frequency
Uses a combined congestion detection mechanism based on
  Average Node delay  based on Channel contention level  computes from exponential weighted moving average of elapsed time
  Local buffer level
Ti  Amount of time needed to provide delay-constrained event reliability for a decision interval i
Tsa Application-speciﬁc communication delay bound
I = DRi/DR*  Delay-constrained reliability Indicator

## Slide 47
Based on the current status fi+1 is adjusted as
  Early Reliability and No Congestion (Ti < Tsa and CN = 0)
  Early Reliability and Congestion (Ti < Tsa and CN = 1)
  Low Reliability and Congestion (Ti > Tsa and CN = 1)
  Adequate Reliability and no congestion
  (f < fmax and 1- ≤I ≤1+ and CN = 0)

## Slide 48: Qualitative Evaluation
Merits
  Self-conﬁguring
  Performs efﬁciently under random, dynamic topology
  Achieves real-time and reliable delivery
  Average energy consumed per packet during communication is decreased as the [No Congestion, Adequate Reliability] state is approached through reporting rate control.
  Addresses congestion control and timely event transport reliability objectives
Demerits
  protocol operation is based on feedback from the sink, where a broadcast medium is assumed for the downstream trafﬁc. However, this may not be applicable to deployments where multi-hop communication is necessary.
  Similar to ESRT, the same reporting frequency value is used for all sensors in a decision interval. This approach may not be suitable for networks where local interactions vary the network conditions signiﬁcantly.