## Slide 1: Query Processing and Data Aggregation

## Slide 2: Energy Consuming Parts of Sensor Network
Sensor Transducer
  Responsible for capturing environmental parameters
  Samples measured physical data and converts them into electrical signals
Embedded Processor
  Equipped with memory and responsible for controlling the sensing, computation, and communication units
  Two types of energy consumed in this component: switching energy and leakage energy.
  The switching energy is consumed when computation is performed
  The leakage energy is consumed when no computation is being performed.
Transceiver
  Consists of a transmitter for sending data and a receiver for receiving the data from its 1 - hop neighbors.
  Energy is consumed for both transmitting and receiving data

## Slide 3
Spatial Property: The physical parameters sensed by neighboring sensor nodes are similar in nature.
Temporal Property: A sensor node may sense similar data values during consecutive time periods
Remove or reduce the redundancy and transmit the relevant data to the BS or sink.
The process or technique of reducing data redundancy by combining the data from neighboring sensor nodes is called data aggregation
A user requests the BS for relevant information in the form of queries
Two types of routing the data back to the BS
  Address–Centric (AC) routing
  Data- Centric (DC) routing

## Slide 4: Query Characteristics
Types
  Query Request
  Query Response
Structure of Query
  SELECT … FROM … WHERE … GROUPBY … HAVING …
    join, projection, aggregation, grouping
  Sensor Data  A virtual table with one column per sensor type
  Tuples are appended at well-defined intervals
  Time between sample intervals  epoch
  Every sensor query is associated with time interval [S, S+T]
Query Operators
  Types of data: Stored data  relation; Sensed data  sequence
  Sensor query is defined as an acyclic graph of relational and sequence operators
  Relational Operators: insert, delete, modify
  Sequence Operators: insertion of new record

## Slide 5
Query classification
  Frequency of Query Response
    Historical Query – used for analysis of historical data
    One-time Query – instantaneous  only one response  same start and end time
    Persistent Query – monitoring for a continuous period  start time “now”, end time “infinity”
  Nature of Search Space
    Spatial
      SELECT attr_val FROM sensor WHERE loc = (20, 30).
    Temporal
      SELECT attr_val FROM sensor WHERE time = 6:50 am – 2:30 am
    Spatio-Temporal
      SELECT attr_val FROM sensor WHERE loc = (40, 25) and time = 1:30 pm – 4:30 pm

## Slide 6
Semantic Nature of Query Response
  Exploratory Query
    Return the record on 01 18 - 07 at5:00 pm
  Monitoring Query
    Return all records for 01 - 18 - 07
  Range Query
    Return all days in the month of March when only fan number 1 was on
Range of Data in Query Response
  Filtering Query
  Non-filtering Query
Number of Attributes in Query Request
  One-Dimensional Query
  Multi-Dimensional Query

## Slide 7: Challenges in Query Processing
Query Broadcast
  Single query vs. fragmented query
  One-to-all or level-wise forwarding
  Identifying duplicate queries
  Aggregated data vs.
  individual data
Querying Interface
Efficient DB for Querying
Uncertainty and Transience
in sensor readings
Probabilistic queries and answers

## Slide 8: Sensor Selection for Querying Process
Types of sensors
  Temperature sensor
  Light sensor
  Pressure sensor
Sensor ID, location, timestamp, value of the reading
Sensor selection using
  Group By
  Having
  Where
  Join
  Specific region
  Specific periodicity

## Slide 9: Query Processing Techniques
Warehousing Technique
  Processing of sensor queries is kept completely separate from the access to the underlying sensor network, where the actual data is sensed and stored.
  Involves two processing steps
    Data is extracted from the sensor network in a predeﬁned fashion
    Stored in a centralized database located on a unique front-end server.
    Suitable for processing predeﬁned queries over historical data
Distributed technique
  The query workload determines the data that should be extracted from sensors.
  More ﬂexible because it enables different queries to extract different data from the sensor network.
  More efﬁcient because only relevant data are extracted from the network.
  Efﬁciently utilizes the computing resources on the sensor nodes. The sensor query in this case can be evaluated at the front - end server, in the network itself, at the sensors, or at some mixture of the three.

## Slide 10
Query Flooding
  Full flood
    Answer to the query is guaranteed to reach the originator
    Each node floods the query to all the nodes within its radio range
    Causes unnecessary communication overhead
    Variation: Contact only a fixed set of nodes that are relevant to the query within a predefined spatial window  reduces congestion thereby reduces response time

## Slide 11: Full Flooding

## Slide 12: Spatio-Temporal Window
Two processing phases
  Phase 1:GREEDYDF phase
    Path is found to a node inside STWin for a given query originator (Qo) that can assume the role of query coordinator (Qc) to broadcast the query to all potential sensor nodes
    Route the packet to its neighbor that is closest to Qc.
    Optimal location of Qc is the center of STWin
    Does not assure the establishment of a routing path within STWin
  Phase 2:
    WinFlood: When a node within STWin receives a query, it broadcast the query to all nodes both inside and outside STWin. Flooding stops when the query reaches a node outside STWin
    WinDepth: Employs DFS traversal to individually send the query to the neighbors within STWin only if they have not yet received the query.
    WinFlood is more cost effective since cost of single broadcast is lower than multiple point-to-point messages

## Slide 13
Spatio-Temporal Window

## Slide 14: Directed Diffusion
The data is identified by an attribute value pair
The query response is data centric
The dissemination sets up a gradient which draws the event data toward the disseminators of the queries.
Gradient is specific to the value of the data wanted and the direction in which the data needs to be sent.
Eg. Query: type=temparature, interval=10ms, duration=40s, Rect = [-200,200,400,600]
DD exploits the spatio-temporal correlation
More applicable for dense, static sensor networks
Not suitable for mobile sensor networks

## Slide 15
Directed Diffusion

## Slide 16: Snapshot Querying
Not all sensors respond to query
Only preselected nodes are allowed to respond to a query
In case of node failure, the surplus standby node responds for the query
The location and values of the representative nodes present the picture of the value distribution in the entire network
Example:
  After receiving a query the neighboring nodes synchronize on a localized basis to select a set (RN )of representative nodes for answering the queries.
  The node Ni with largest number of neighboring nodes is selected as a representative node and in case of tie largest id will be selected.
  If Nj fails or goes out of range of other sensors Ni act as the representative of Nj if d(xj, xi) <= T, where d can be relative, absolute, or sum squared error and T is a pre-specified threshold.
  Ni obtains the reading of every neighbor node Nj either by full flooding or periodic announcements.
  If Ni does not respond or if d(xj, xi) > T then Nj selects new representative node
  Each node Ni maintains a cache line that is updated by cache admission and replacement policies

## Slide 18
Time Series Snapshot
  Used for historical queries like
    Find average humidity in a region1 for the years 1989 to 1994.
  The monitored region is partitioned into a set of sub-regions and the value distribution in each sub region is bounded by a predefined range of the attribute value
  The readings from sensors located closest to the borders of all sub regions are obtained
  The sensors at the surrounding area of boundaries need not transmit data and thereby reduces overall energy consumption

## Slide 19: Acquisitional Query Processing
When and where data should be sampled and how often the sampling should be done.
Query optimization
  To optimize query in terms of cost, time, and power involved in retrieval
  Cost of acquiring a result per second is directly proportional to the cost of executing the query
  Cost of retrieving a reading from a table of query plans is inversely proportional to the selectivity of predicate (: the fraction of rows selected from the table by the predicate if the condition Is satisfied)
  Approaches : Binary Decision Tree, TinyDB

## Slide 20: Binary Decision Tree Approach
A binary decision tree is built on a conditional plan (PTj(x)) which splits the plan at an internal node ni into two alternate condition plans Tj(x)=T and Tj(x)=F
Expected cost of the plan P is the sum of the cost starting from the root node and the expected cost of the value of each new predicate Tj

## Slide 21: Conditional Plan based on time of day

## Slide 22: TinyDB Approach
Uses distributed query processor in each node of sensor network
TinyDB incorporates acquisitional techniques and runs on top of TinyOS.
TinyDB consists of tuples where each tuple denotes one row per node per instant in time with one column per attribute
Queries in TinyDB is of the form SELECT-FROM-WHERE-GROUPBY
Eg. SELECT node-id, pressure, humidity FROM sensors, SAMPLE PERIOD 5s FOR 40s

## Slide 23: Data Aggregation in WSN
Challenges:
  Energy Efficiency: sleep scheduling protocol
  Timing Control: within reasonable time bound
  Application Orientation: based on app. summary, data compression etc. may be used
  QoS Support
Data Aggregation Techniques
  Energy efficient Data Aggregation
  Neural network based Data Aggregation
  Delay Constrained Data Aggregation
  QoS Constrained Data Aggregation
  Data Aggregation for Range Query
  Structure free Data Aggregation

## Slide 24: Energy Efficient Data Aggregation
Use of simple mathematical operators
  Provides estimated value of the population
  SUM, COUNT
  Gradual aggregation when the data goes up along the tree.
Aggregating Object Report at Source
  Aggregate at the source and send the report back to BS.

## Slide 25: Neural Network Based Data Aggregation
By using dimensionality reduction
Achieved by employing neural network based algorithm which runs on an iterative pattern of adjusting weights to learn regular inputs.
Instead of reporting raw data, specific sensory input pattern is classified and is sent
FuzzyART (Adaptive Resonance Theory)
The input layer F0 stores input bits and transmits it to category layer F2 via comparison layer F1
Each input pattern is compared with each category node ni and an activation Ti is calculated for each category node. The node with maximum Ti ‘s weight is compared the input at F1. If the matching condition satisfies a threshold (), then ni captures the current input and updates its weight.
The comparison cycle continues until a stored category is found matching the input pattern. If not the network learns a new category by assigning a new category node in F2.

## Slide 27
Es – energy savings in communication
n – No. of sensors in cluster unit
k – No of sensors reporting to CH
r – size of raw sensor data
c – No. of bytes to represent a category

## Slide 28: Delay Constrained Data Aggregation
Timing control problem due to delay incurred in collecting data from neighborhood
Data Aggregation Tree (DAT) based approach
  Different tree nodes respond to a query with different delays depending on the tree levels at which they are located.
  To reduce delay
    FSM based feedback control scheme
      Waiting time at each level of tree is adjusted according to the output of FSM while maintaining substantial level of accuracy
      Initial part of FSM waits for larger time.
      When accuracy level reaches a stable value, the waiting time is adjusted to control delay.

## Slide 30
Variants of FSM based scheme
At each step of calculation in the aggregation period, the optimal number of messages received is compared with the actual number received. If fewer messages are received, the aggregation period is increased by one unit. Otherwise decreased by one unit
Change the parameter to the performance and based on the difference between the actual number of received responses and the desired optimal number of responses.
This decision is made based on whether the aggregation period needs to be changed at a faster speed, instead of the addition/subtraction operations at the FSM.
Data responses are sent bottom - up starting from the leaf nodes to the sink. Each data response contains some extra information, indicating the total number of responses that have been aggregated into a single message.
Based on this information, the next aggregation period Tn+1 is calculated as

## Slide 31: QoS Constrained Data Aggregation
Sending reports to BS is deferred to meet
  End-to-end latency
  Measurement accuracy
The intermediate nodes independently decide whether or not to perform data aggregation based on resource conditions and task requirements
No clustering or tree formation is required
When and where to perform the task is based on availability of local information
If the QoS requirement for end-to-end delay is at most D, but the packet received at intermediate hop already exceeded the constraint, the packet is discarded
Three cases upon receiving a packet
  If the delay constraint can be satisfied, the intermediate node (aggregator) defers the report for a pre-specified time interval with a pre-specified probability, during which it processes and aggregates any packets that arrive and generates a new packet before transmitting it to the next hop.
  If the delay constraint can be satisfied only if the report is not deferred, the aggregator tries to forward this report to the next hop.
  If the delay constraint cannot be satisfied in any case, the aggregator discards the report to avoid further wasting of any additional resources.
Trade off between Energy efficiency, Delay requirement, accuracy and buffer overflow probability
Packet Delivery Probability higher with discard strategy
Energy consumption decreases as deferred time increases
Network lifetime increases
Reduced comm. Due to increased aggregation
Average delay increases

## Slide 32: Data Aggregation for Range Query
Combines data aggregation and dissemination
Network consists of
  mobile sinks which request nearby static sensors to sense event data,
  specific sensor in a grid, which has knowledge about the event, is designated as the head of the grid.
For a regular - shape range query, a mobile sink designates the range (e.g., a range of rectangle) for data aggregation, and requests the source (i.e., a static sensor sensing data) to collect the data in the designated range.
The head of the grid, called agent, receives the aggregated data from the source and sends the data to the mobile sink.
The aggregated data from a source, which are a collection of packets reported to all the children of the source, are reported to the nearby head of the grid.
To account for its mobility and to ensure that the mobility does not affect the data transmission, a mobile sink receives data from the source constantly.
It checks its location every second and if it detects that it moves out of the original grid, it chooses the head of the new grid as a new agent.
An irregular - shape query is used to monitor and collect the data of the diffusing event, that is, the event data from another neighbouring grid that may diffuse into the grid in question.
A cache mechanism is used to resolve the identical queries issued from mobile sinks. The protocol can reduce the overall energy consumption of the network.

## Slide 33: Structure-Free Data Aggregation
Maintaining hierarchical structure introduces additional cost, in case of mobile sensor networks
  In a dynamic environment, mobile sensors may frequently go out of the transmission range and a new structure needs to be built more often, leading to high maintenance overhead. This problem may also arise if a static sensor in the hierarchical structure runs out of energy and disconnects the topology.
Opportunistic (OP) aggregation: Data packets are aggregated only if they happen to meet at a sensor at the same time, which leads to inefficiency in the aggregation process.
In the OP approach, there is no pre-specified set of aggregation nodes for combining the data, which leads to last minute routing decisions to be taken and thus becomes time consuming.
To alleviate both problems, a structure - free data aggregation approach is proposed
To increase aggregation efficiency, a MAC protocol called data - aware any cast (DAA) is also proposed because packets need to be aggregated early on their way to the BS.
If some nodes wait for other nodes to send data it can lead to efficient aggregation. Hence Randomized waiting is used.

## Slide 34
Conditions for Data aggregation
  Spatial Convergence
  Temporal Convergence
DAA improves spatial convergence and RW improves temporal convergence
In DAA
  An independent set among sources is created
  Nodes are assumed to be synchronized in time.
  All nodes aggregates at the same time
  Nodes in independent set act as aggregator and are created on the fly when data is transmitted to BS
Reduces extra overhead in structure creation
Each packet has aggregation ID (AID) used as the metric for aggregation
Uses RTS/CTS and anycast mechanisms in MAC
RTS contains AID and any neighbor with same AID responds with CTS.
Those packets are aggregated
To achieve temporal convergence Random Waiting is used
  RW introduces artificial delay at the sources and thereby increases temporal convergence.
  DAA + RW outperforms OP