## Slide 1: OPERATING SYSTEMS FOR WIRELESS SENSOR NETWORKS

## Slide 2: Operating System Design Issues
Process Scheduling: Earliest Deadline first (EDF) or its variants for process scheduling. Context switching in WSN is costlier
Memory Management: Exclusive memory for each process / task helpful for protection / security but WSN has small memory. Sol.- sharing of memory
Kernel Model – Micro kernel designed using Event-driven and finite state machine model
  Event Dirven  receiving a packet, transmitting a packet, detection of event of interest, alarms about energy depletion of sensor node
  FSM based  to realize concurrency, reactivity and synchronization
API – Modular and general API for applications. APIs should enable the applications access underlying hardware
Code Upgrade and reprogramming: Behaviour of sensor node and their algorithms need to be adjusted for their functionality or for energy conservation  OS should be able to reprogram and upgrade
No external disk  No file system

## Slide 3: OS Design Issues
Should be compact and small in size
Should provide real-time support . Information should be collected and reported as quickly as possible
Should provide fair and efficient resource management mechanism to allocate microprocessor time and limited memory
Should support reliable and efficient code distribution since the functionality of sensor node may be changed after deployment
Bandwidth utilization must be as little as possible
Should provide a generic programming interface up to sensor middleware or application software

## Slide 4: Example OS
Tiny OS
Mate
Magnet OS
MANTIS
OSPM
EYES OS
SenOS
EMERALDS
PicOS

## Slide 5: Tiny OS
Allows application software to access hardware directly when required
microthreaded OS
Addresses 2 issues:
  How to guarantee concurrent data ﬂows among hardware devices
  How to provide modularized components with little processing and storage overhead.
Uses an event-based model to support high levels of concurrent application in a very small amount of memory.
Achieves higher throughput since the context switching is faster than stack based approach
Rapidly create tasks associated with an event, with no blocking or polling.
When CPU is idle, the process is maintained in a sleep state to conserve energy.
Tiny OS has a tiny scheduler and a set of components
Scheduler schedules the operation of those components
Each component has 4 parts:
Command handlers, Event handlers, encapsulated fixed size frame and a group of tasks

## Slide 6: Tiny OS
Commands and tasks are executed in the context of the frame and operate on its state
Each component declares its commands and events to enable modularity and easy interaction with other components
Uses a simple FIFO
Data structure used is very simple and power efficient.
Allows the processor to sleep when the task queue is empty
Frame is fixed in size and is assigned statically.
Specifies memory requirement of a component at compile time and no dynamic assignment overhead.
All commands are non-blocking requests made to low-level components
Occurrence of a hardware event invokes event handlers
Event handler store information in its frame, assign tasks and issue high-level events or call low-level commands
Commands and events are used to perform a small fixed amount of work as well as to preempt tasks

## Slide 7: Tiny OS
Tasks calls low-level commands, issue high-level events and assign other tasks
Through tasks arbitrary computations are performed
Three types of components:
  Hardware abstraction  Lowest level components. Each component is mapped to a hardware abstraction. I/O devices, Radio transceivers, and sensors
  Synthetic Hardware  To map the behavior of advanced hardware and sit on the hardware abstraction
    Hardware abstract component - Radio Frequency Module (RFM) for transceiver
    Synthetic hardware component – Radio byte – handles data into or out of the underlying RFM
  High-level software components

## Slide 8: Advantages of TinyOS
Requires very little code and a small amount of data
Events are propagated quickly and the rate of posting a task and switching the corresponding context is very high
Provides efficient modularity

## Slide 9: Mate
Designed to work on the top of TinyOS as one of its components.
Byte-code interpreter
  Make TinyOS accessible to non-expert programmers and to enable quick and efﬁcient programming of an entire sensor network.
Provides an execution environment for the UC–Berkeley mote
Program code is made up of capsules.
Each capsule has 24 instructions, and the length of each instruction is 1 byte.
The capsules contain type and version information to make code injection easy.
Capsules can deploy themselves into the network.
Mate implements a beaconless (BLESS) ad hoc routing protocol as well as the ability to implement new routing protocols.
A sensor node that receives a newer version of a capsule installs it.
Through hop-by-hop code injection, Mate can program the entire network.
Capsules are classiﬁed into four categories:
  message send, message receive, timer, and subroutine.
An event can trigger Mate to run.
It can be used as a virtual machine platform for application development and also as a tool to manage and control the entire sensor network.

## Slide 10: MagnetOS
Distributed adaptive operating system designed speciﬁcally for application adaptation and energy conservation.
Goals:
  To adapt to the underlying resource and its changes in a stable manner
  To be efﬁcient with respect to energy conservation
  To provide general abstraction for the applications
  To be scalable for large networks.
Single system image (SSI) or a single uniﬁed Java virtual machine that includes static and dynamic components.
The static components rewrite the application in byte-code level and add necessary instructions on the semantics of the original applications.
The dynamic components are used for application monitoring, object creation, invocation, and migration.
SSI abstraction provides more freedom in object placement and simpliﬁes application development.
Provides an interface to programmers for explicit object placement and override of the automatic object placement decisions.
Provides two online power-aware algorithms (NetPull and NetCenter) for use in moving application components within the entire network so as to reduce energy consumption and extend network lifetime.
Netpull works hop by hop at the physical layer, and NetCenter runs multi hop at the network level.
The difference between traditional ad hoc routing and NetPull (NetCenter) is that the communication endpoints in ad hoc routing are ﬁxed, whereas NetPull tries to move the communication endpoints in order to conserve energy

## Slide 11: MANTIS
Multithread embedded operating system
General single-board hardware enables ﬂexible and fast deployment of applications.
Uses classical layered multithreaded structure and standard programming language.
The layered structure contains multithreading, preemptive scheduling with time slicing, I/O synchronization via mutual exclusion, a network protocol stack, and device drivers.
Kernel realizes these functions in less than 500 bytes of RAM. Uses standard C to implement the kernel and API.
RAM size allocated to each new thread is ﬁxed.
The thread table stored in a global data structure has a capacity for of items, each of which is 10 bytes and is used to store thread-related information.
The thread scheduler s priority based and round robin within each priority level.
The scheduler is triggered only by timer interrupts from hardware to perform context switching. Other interrupts are handled by device drivers.
The network protocol stack has four layers: application, network, MAC, and physical.
Implements ﬂooding as a routing protocol and a simple stop-and-wait protocol for ﬂow and congestion control
The total code size of the kernel, scheduler, and network stack is smaller than 500 bytes and 14 kB ﬂash.
Advanced features supported:
  Multimodal prototyping environment for testing sensor networking applications,
  dynamic binary update-based reprogramming,
  remote shell and command server enabling the user to log in and inspect the sensor node’s memory and status.

## Slide 12: OSPM
OSPM (or dynamic power management, DPM),
Directed at power management techniques.
Based on a greedy algorithm that will switch the system to a sleep state as soon as it is idle.
It considers the following factors
  Transitioning to a sleep state has the overhead of storing the processor state and shutting off the power supply.
  Waking up takes a ﬁnite amount of time.
  The deeper the sleep state, the less the power consumption will be lower and the wake-up time will take longer
Based on a given event arrival model, transition time, and power consumption rate, it reduces the energy savings.
If the energy savings is positive, it will trigger a state transition; otherwise, the current state is maintained.
Adaptive shutdown algorithm is a trade-off between energy savings and the cost of delay and possibly missed events.

## Slide 13: EYES OS
Uses an event-driven model and task mechanism
Works in a simple sequence:
  perform a computation, return a value, and enter the sleep mode.
Task can be scheduled using a FIFO-, priority-, or deadline-based approach (such as EDF), and is triggered by events in a non-blocking manner.
Deﬁnes an application programming interface (API) locally and for the network components.
The local information component provides functions such as access to sensor node data, availability of resources and their status, and setting of parameters or variables in sensor nodes.
The network component provides functions to transmit and receive data and to retrieve network information.
Realizes two groups of functions:
  Those that can be executed at boot time to upload software module,
  Those that can provide node localization information.

## Slide 14: EYES OS
Provides an efﬁcient code distribution mechanism
  to update the code on the sensor node, including the operating system;
  to be resilient in case of packet loss during update
  to use as few communications and local resources as possible
  to halt the application for a short period when updating.
The procedure to distribute code is performed in four steps:
  initialization, code image building, veriﬁcation, and loading.
Three options for updating the running code:
  halved memory, a two-phase approach, and built-in EEPROM, which is used by EYES OS.

## Slide 15: Sen OS
Finite state machine (FSM)–based operating system.
It has three components:
  A kernel that contains a state sequencer and an event queue.
    The state sequencer waits for an input from the event queue (a FIFO queue).
  A state transition table that keeps the information on state transition and the corresponding callback functions.
    Each state transition table deﬁnes an application.
    Using multiple state transition tables and switching among them, supports multiple applications in a concurrent manner.
  A callback library of call functions.
    An incoming event will be queued in the event queue.
    The ﬁrst event in the event queue is scheduled, which triggers a state transition and correspondingly, invokes the associated functions.
The kernel and callback library are statically built and stored in the ﬂash ROM of a sensor node.
The state transition table can be reloaded or modiﬁed at runtime since it is application dependent.

## Slide 16: EMERALDS
It is an extensible microkernel written in C++ for embedded, real-time distributed systems with embedded applications running on slow processors (15 to 25 MHz) and with limited memory (32 to 128 kB).
It supports multithreaded processes and full memory protection, which are scheduled using combined earliest deadline ﬁrst (EDF) and a rate-monotonic (RM) scheduler.
The device drivers are implemented at the user level, whereas interrupt handling takes place at the kernel level.
EMERALDS uses semaphores and condition variables for synchronization with priority inheritance at the same time and provides full semaphore semantics to reduce the amount of context switching.
Inter-processor communication (IPC) is realized by using global variables to exchange information between tasks.
It does not consider networking issues

## Slide 17: PicOS
Written in C for a microcontroller with limited on-chip RAM (e.g., 4 kB).
All tasks share the same global stack and act as co-routines with multiple entry points and implicit control transfer, which is different from classical multitasking approaches.
Each task is like a FSM where the state transition is triggered by events.
The FSM approach is effective for reactive applications whose primary role is to respond to events rather than to process data or crunch numbers
The CPU cycle is multiplexed among multiple tasks, but the tasks can be preempted only at the FSM state boundary.
It has few resource requirements and supports multitasking,
Not good for real-time applications.