## Slide 1: Distributed Topology Control
Design Guidelines

## Slide 2: Distributed Topology Control
Given the node locations, identify optimal network topologies with respect to a certain metric like energy cost, energy efficient unicast / broadcast
Ideal Features of Topology Control Protocol
  Fully distributed and Asynchronous
  Localized
  Rely on bidirectional links
  Preserve connectivity
  Generate topology with small physical node degree
  Rely on low quality information

## Slide 3: Future Trends in Wireless Sensor Network

## Slide 4: Future Trends in WSN
WSN performing specialized tasks
  Wireless Multimedia Sensor Networks
  Wireless Sensor and Actor Networks
WSN in Challenging Environment
  Underwater Acoustic Sensor Networks (UW-ASN)
  Wireless Underground Sensor Networks

## Slide 5: Wireless Multimedia Sensor Networks
SNs that communicates video and audio streams, still images and scalar sensor data
Requirements
  Store, process in real time, correlate, and fuse multimedia data originated from heterogeneous sources
  Deliver multimedia content with certain level of QoS
Challenges
  Sensors have limited battery, memory processing capability and data rate
  Capacity of each link is fixed and predetermined
  Attainable capacity of the wireless link in multi hop wireless network depends on the interference level perceived at the receiver
  Interference level depends on the interaction of functionalities that are handled by all network devices in a distributed manner
  Capacity and delay attainable on each link are location dependent, vary continuously and may be bursty in nature
  Cross layer interactions must be provided to support QoS
  In-network processing of multimedia content should be supported

## Slide 6: Applications of WMSN
Multimedia Surveillance Sensor Networks
Traffic Avoidance, Enforcement, and Control Systems
Advanced Health Care Delivery
Environmental Monitoring
Industrial Process Control

## Slide 7: Factors that influence design of WMSN
Application Specific QoS Requirement
  Snapshot type:- contains event triggered observations obtained in a short period of time
  Streaming Multimedia type:- sustained information delivery for long duration of time
  QoS: Bounds on energy consumption, delay, reliability, distortion, network lifetime
High bandwidth demand
Multimedia In-Network Processing
Power Consumption
Flexible architecture to support heterogeneous applications
Multimedia Coverage
Integration with Internet Architecture
Integration with other wireless technologies

## Slide 8: Ultra Wideband Technology
Bandwidth of around 500 MHz
Requires low-power
Supports high data rate
Limited coverage area (within tens of meters)
More suitable for WSNs
As per FCC regulation - Spectrum around 3.1 to 10.6 GHz
But can use entire frequency spectrum with limited interference, since coverage area is very less

## Slide 9: UWB Approaches
Time-hopping impulse radio UWB (TH-IR-UWB)
  Based on sending very short duration pulses in the order of hundreds of picoseconds)
  Time is divided into frames
  Each frame consists of several chips of very short duration
  Each sender transmits one pulse in a chip per frame and multiuser access is provided by pseudo random time hopping sequences that determine in which chip each user should transmit
Multi Carrier UWB (MC-UWB)
  Uses multiple simultaneous carriers
  Based on orthogonal frequency division multiplexing (OFDM)
  Well suited for avoiding interferences since carrier frequencies can be chosen to avoid narrowband interference to or from narrowband systems
  High speed FFT processing is necessary  Requires high processing power  complex transceivers

## Slide 10: TH-IR-UWB
Requires fast switching time for transmitter and receiver
Requires highly precise synchronization
Interference of UWB with other system is less because of high instantaneous power during short interval
But probability of interference between two UWB signals is high
Least cost transceivers
Best suited for WSNs due to high data rate and very low power consumption, simple design, and low cost
Has fine delay resolution property by exploiting more resolvable paths in Multipath environment
Provides large processing gain in the presence of interference
Provides flexibility since data rate can be traded for power spectral density and multipath performance
Easy to find suitable codes for THS and no assignment protocol is necessary
Allows for integrated MAC/PHY solutions
Interference mitigation techniques allows simultaneous senders
Simultaneous senders possible without complex receivers as in CDMA
Large instantaneous bandwidth enables fine time resolution for accurate position estimation and for network time distribution
Has low probability of interception / detection, i.e. highly secure

## Slide 11: Cross Layer Design
Commonly used MAC in WSN: Carrier sense multiple access with collision avoidance (CSMA/CA)
CSMA/CA requires mutually exclusive transmissions, that is, when a device is receiving data, transmissions from all the devices in its transmission range are impeded.
Mutual exclusion - carrier sense and random timers
Random timers  introduces delay
carrier sense  introduces energy wastage for idle listening; collisions occur due hidden node problem
Introducing sleep periods to reduce idle listening reduces the energy consumption at the expense of latency and coordination complexity.
Cross–layer communication architecture: To reliably and ﬂexibly deliver QoS to heterogeneous applications in WMSNs with limited interactions among the functionalities of different layers.
The architecture is based on the TH–IR–UWB transmission technique

## Slide 12: Design Principles of Cross Layer Design
Network Layer QoS Support Enforced by a Cross - Layer Controller
Provides packet - level service differentiation in terms of throughput, end-to-end packet error rate, and delay.
XLCU conﬁgures and controls the networking functionalities at the physical, MAC, and network layers by using a uniﬁed logic that makes decisions based on
  application requirements speciﬁed by the application layer;
  status of the functional blocks implementing the networking functionalities.
Without sacriﬁcing on upgradeability, modularity, and ease of system design.

## Slide 14: Design Principles
Geographical Routing
  Time - based approaches in UWB allow ranging accuracy on the order of centimeters .
  Hence, the geographical routing module leverages geographical information to provide QoS.
  Positioning capabilities are needed in sensor networks to associate the physical meaning with the information gathered by sensors.
  Knowledge of the position of each network device allows for scalable routing solutions.
Hop-by-Hop QoS Contracts
  End - to - end QoS requirements are enforced through local interactions.
  Each device is responsible for locally guaranteeing given performance objectives.
  The global end -to-end requirement is guaranteed by the joint local decisions made by the participating devices.

## Slide 15: Design Guidelines
Receiver - Centric Scheduling for QoS Trafﬁc
  In multi-hop wireless environments, interference is location dependent.
  QoS is provided through receiver - centric scheduling.
  A receiver can be responsive to the dynamics of the channel based on local measurements and consequently control loss recovery and rate adaptation, thus avoiding feedback overheads and latency.
UWB Physical/ MAC Layer
  Integrated MAC and physical layer based on UWB.
  TH-IR-UWB allows multiple transmissions in parallel.
  This allows devising MAC protocols with minimal coordination.
  TH-IR-UWB transceivers are simple to implement.
Dynamic Channel Coding
  Power control is not beneﬁcial in TH-IR-UWB.
  Adaptation to interference at a receiver is achieved through dynamic channel coding, which can be considered as an alternative form of power control because it modulates the energy per bit based on the interference perceived at the receiver

## Slide 16: Wireless Sensor and Actor Networks
WSAN is a heterogeneous network composed of embedded devices, where a subset of the devices (sensors) gather environmental information and another set of more powerful and less resource constrained devices (actors) physically manipulate the environment and interact with it.
Distributed WSANs are capable of observing the physical world, processing the data, making decisions based on the observations, and performing appropriate actions/tasks.
In WSANs, the sensing and acting tasks are performed by sensor and actor nodes, respectively.
Sensors are low - cost and low - power devices with limited sensing, computation, and wireless communication capabilities.
Actors are resource - rich devices equipped with better processing capabilities, higher transmission powers, and longer battery lifetime.
Number of sensor nodes deployed in a target area may be on the order of hundreds or thousands, whereas such a dense deployment is usually not necessary for actors because actors have higher capabilities and can act on large areas.
Actor vs. Actuator
  An actuator is a device to convert an electrical control signal to a physical action and may be used for ﬂ ow - control valves, pumps, positioning drives, motors, switches, relays, and meters. It constitutes the mechanism by which an agent acts upon the physical environment.
  An actor, is able to act on the environment by means of one or several actuators, is also a single network entity that performs networking - related functionalities, that is, receive, transmit, and relay data.

## Slide 17: Requirements of WSAN Protocols
After the sensors detect an event that is occurring in the environment, the event data is processed and transmitted to the actors in a distributed manner
Sensors gather, process, and eventually reconstruct the event data.
The process of establishing data paths between sensors and actors is referred to as sensor –actor coordination.
Once the event is detected, the actors coordinate to reconstruct its data, estimate its characteristics, and make a collaborative decision on how to perform the action. This process is referred to as actor–actor coordination
The operation of a WSAN can be thought of as an event-sensing, communication, decision, and acting loop, whose objective is to timely react to sensor information with an effective action.
Real time coordination and communication is an important concern in WSANs to guarantee the timely execution of correct actions.
The energy efﬁciency of network communications is also crucial because sensors are resource – constrained nodes with limited battery lifetime.
Sensor network protocols and algorithms should be scalable and localized because the number of nodes can be arbitrarily high.

## Slide 18: Applications of WSAN
The performed actions serve the purpose of enhancing the operation of the sensor network by enabling or extending its monitoring capability.
Applications where actors are part of the network and perform actions based on the information gathered by sensors.
  Battleﬁeld surveillance, nuclear, biological or chemical attack detection, home automation, and environmental monitoring
  Fire detection applications: sensors can relay the exact origin and intensity of the ﬁre to water sprinkler actors that will extinguish the ﬁre before it spreads.
  Sensors can detect plumes; that is, visible or measurable discharges of contaminants in water or in the air, and actors can reactively take countermeasures.
  Motion, acoustic, or light sensors in a building can detect the presence of intruders and command cameras or other instrumentations to track them.
  Mobile actors can be moved to the area where the intruder has been detected to get high resolution images and prompt or block the intruder.

## Slide 19: Sensor-Actor Coordination
Sensor – actor coordination is designed on an event - driven clustering paradigm, where cluster formation is triggered by an event and clusters are created on the ﬂy to optimally react to the event
Sensors detecting an event coordinate to optimally associate each sensor with an actor.
Only the event area is clustered and each cluster consists of those sensor nodes that send their data to the same actor.
Architecture:

## Slide 20: Sensor-Actor Coordination
Latency bound B is the maximum allowed time between the instant when the physical features of the event are sampled by the sensors and the instant when the actor receives a data packet describing these event features.
A data packet that does not meet the latency bound B when it is received by an actor is said to be expired and thus unreliable.
A data packet received within the latency bound B is said to be unexpired and is reliable.
The event reliability r is the ratio of reliable data packets over all the packets generated in a decision interval.
Whenever one or more packets are dropped by an intermediate sensor, the actor is notiﬁed about the lost packet(s) in the header of the next data packet so that the packet loss can be taken into account in the computation of the reliability. The event reliability threshold r th is the minimum event reliability required by the application.

## Slide 21: DECR Protocol for Sensor Actor Coordination
Distributed event - Driven clustering and routing (DECR) protocol.
Scalable and reliable
Sensor – actor coordination problem consists of establishing data paths from each sensor residing in the event area to the actors by
  Ensuring that the observed reliability r is above the event reliability threshold rth (i.e., r > rth)
  Minimizing the energy consumption associated with data delivery paths.
The objective of the optimization problem is to ﬁnd data aggregation trees (da - trees) from all the sensors that reside in the event area (referred to as sources) to the appropriate actors.
A da - tree is composed by aggregating individual ﬂows , where a ﬂow is deﬁned as a connection between a sensor and an actor.
The optimal strategy for event - driven clustering is formulated as an integer linear program (ILP).
The objective of the protocol is to build energy - efﬁcient da - trees between the sources that reside in the event area and the actors to provide the required reliability rth with minimum energy consumption.
Based on the observed reliability that each actor advertises, the protocol favors a local behavior for each individual sensor node that results in a global network behavior compliant with the application requirements; that is, provide event reliability r above the required threshold rth and minimize the energy consumption.
The reliability is controlled based on the idea of adjusting the delays by modifying the average end - to - end path length.

## Slide 22: DECR
Consists of three states:
  Start-up, Speed-up, and aggregation
Three simulation scenarios
Scenario 1
  Deployment area: Circular – radius 20m
  For each sensor, the distance from the center of the area and the angle are uniformly distributed random variables
Scenario 2
  Sensors are deployed randomly in a square area of 25m x 25m.
  The event area is circular with varying radius in [2,12] m
Scenario 3
  Equivalent to 2but the square area is 100m.
Four actors are randomly deployed in each scenario
Transmission range of sensors – 10m

## Slide 23: Simulation Results of DECR
The optimal solution is almost independent of the event range.
  Since the number of sources increases when the event range increases, leads to a potentially higher energy consumption;
  Since more nodes are involved, aggregation can be increasingly leveraged.
The energy consumption in the start–up and speed-up conﬁgurations highly increases with the event range.
The energy consumption of the aggregation conﬁguration is two orders of magnitude lower than in the start–up conﬁguration.
The energy consumption increases sub-linearly with the number of sensors.
The energy consumption of the speed-up conﬁguration is around one order of magnitude higher than in the start-up conﬁguration
When the aggregation conﬁguration is reached from a speed-up conﬁguration, the network converges to a less energy-efﬁcient conﬁguration, compared to when the aggregation conﬁguration is reached directly from the start–up conﬁguration.

## Slide 24: Actor-Actor Coordination
Objective: To select the best actor(s) to perform appropriate action on the event area.
Similar to multi-robot task allocation (MRTA) problem
  Which robot should execute which task in order to cooperatively achieve the global goal ?
At the end of the sensor–actor coordination phase, one or multiple actors, which are called collectors , receive sensor readings from the sources that sense the event. These sources deﬁne the event area .
The event area corresponds to the action area ; that is, the area where the actors should act.
Each collector receives data from a subset of the sources (cluster).
Each cluster area identiﬁes a portion of the action/event area and is under the responsibility of the corresponding collector.
Collector may not be able to act on its entire responsible area; that is, this area may not be entirely within the collector ’ s action range .
The action range deﬁnes the circular area where an actor is able to act.
Collector may not be the “best” actor for that task in terms of action completion time and/or energy consumption , where the former is the time to perform the action and the latter is the energy consumed for the action.

## Slide 25: Simulation Results
The coordination objective of multiple collector actors is to ﬁnd the optimal actors to timely act on the portion of the event area under their own responsibility.
Distributed solution to the actor – actor coordination problem is based on a real - time auction protocol that describes the behavior of the actors participating in transactions as buyers/sellers.
The objective of the auction is to select the best set of actors to perform the action on each overlapping area , deﬁned as an area where multiple actors can act upon.
Three approaches: optimal , 1-actor , and localized auction .
In the optimal solution, the best set of actors is chosen so that the average residual energy of the involved actors is maximized, while guaranteeing that the action is completed before the action completion time.
In the 1-actor heuristic, the action is performed by one actor only for each overlapping area; that is, the actor with the highest residual energy after the completion of the action.
In the localized auction each overlapping area is taken care of by an auctioneer that divides it among the actors based on their bids.
Two scenarios with three overlapping areas, one with homogeneous actors and one with heterogeneous actors (half of which are low - efﬁciency actors, while the other one–half are high - efﬁciency actors).
The localized auction mechanism leads to near–optimal residual energy, as each auctioneer calculates the optimal solution separately for its overlapping area. Achieved with local communications among actors.
In the heterogeneous scenario, the proposed localized solution effectively exploits the high - efﬁciency actors, thus reducing the dissipated energy to complete the action.

## Slide 26: Underwater Acoustic Sensor Networks
Applications of UW – ASN
  ocean sampling, environmental monitoring, undersea explorations, disaster prevention, seismic monitoring, equipment monitoring, assisted navigation, distributed tactical surveillance, and mine reconnaissance.
Physical Layer Technology: Acoustic communications
Traditional approaches : Ocean-bottom or ocean–column monitoring is to deploy underwater sensors that record data during the monitoring mission and then recover the instruments
Disadvantages:
  Recorded data cannot be accessed until the instruments are recovered, which may happen several months after the beginning of the monitoring mission.
  Interaction between onshore control systems and the monitoring instruments is not possible, which impedes any adaptive tuning or reconﬁguration of the system.
  If failures or misconﬁgurations occur, it may not be possible to detect them before the instruments are recovered.
  The amount of data that can be recorded by every sensor during the monitoring mission is limited to the capacity of the onboard storage devices.
Solution: To deploy and connect untethered underwater instruments by means of wireless links that rely on acoustic communication

## Slide 27: Challenges in the design of UWASN
The available bandwidth of the underwater channel is severely limited.
The underwater channel is impaired because of multipath and fading.
Propagation delay is ﬁve orders of magnitude higher than in radio frequency (RF) terrestrial channels.
Variable and high bit error rates as well as temporary losses of connectivity (shadow zones) can be experienced.
Batteries of underwater sensors have limited power and usually cannot be recharged.
Underwater sensors are prone to failures because of fouling and corrosion.

## Slide 28: Difference between Terrestrial sensor networks and underwater sensor networks
Parameter | TSN | UWASN
Cost | Less | Higher
Deployment | Dense | Sparse
Power | Less | Higher
Memory | Limited memory | Large memory
Spatial Correlation | Highly Correlated | Less Correlated

## Slide 29: Classification of UW communication links
Based on range
  Very Long
  Long
  Medium
  Short
  Very Short
Based on direction of sound ray w.r.t. ocean bottom
  Horizontal
  Vertical

## Slide 30: Factors influencing the design of underwater Protocols
Transmission Loss:
  Due to attenuation and geometric spreading .
  Attenuation is mainly provoked by absorption due to conversion of acoustic energy into heat, and increases with distance and frequency.
Noise:
  man - made noise : Mainly caused by machinery noise and shipping activity
  ambient noise: Related to hydrodynamics, and to seismic and biological phenomena.
Multipath Propagation:
  Responsible for severe degradation of the acoustic communication signals because it generates inter Symbol interference (ISI).
  The multipath geometry depends on the link conﬁguration. Vertical channels are characterized by little time dispersion, whereas horizontal channels may have long multipath spreads.
High Delay and Delay Variance:
  The propagation speed in the UW – A channel is ﬁve orders of magnitude lower than in the radio channel. This large propagation delay (0.67 s/km) and its variance reduces the system throughput.
Doppler Spread:
  The Doppler frequency spread is signiﬁcant in UW - A channels , causing degradation in the performance of digital communications.

## Slide 31: Communication Architecture of UWASN

## Slide 32
A group of sensor nodes are anchored to the bottom of the ocean.
Underwater sensor nodes are interconnected to one or more underwater gateways (UW-gateways) by means of wireless acoustic links.
UW-gateways are network devices in charge of relaying data from the ocean bottom network to a surface station.
UW-gateways are equipped with two acoustic transceivers, namely, a vertical transceiver and a horizontal transceiver.
The horizontal transceiver is used by the uw – gateways to communicate with the sensor nodes in order to
  send commands and conﬁguration data to the sensors (uw gateway to sensors);
  collect monitored data (sensors to uw - gateway).
The vertical transceiver is used by the uw – gateways to relay data to a surface station. In deep water applications,
vertical transceivers must be long – range transceivers.
The surface station is equipped with an acoustic transceiver that is able to handle multiple parallel communications with the deployed uw -gateways.
It is also endowed with a long range RF and/or satellite transmitter to communicate with the onshore sink (os -sink) and/or to a surface sink (s sink).
In shallow water, bottom-deployed sensors/modems may directly communicate with the surface buoy, with no specialized bottom node (uw -gateway).

## Slide 33: 3D Communication Architecture

## Slide 34
Three - dimensional (3D) underwater networks are used to detect and observe the phenomena that cannot be adequately observed by means of ocean bottom sensor nodes; that is, to perform cooperative sampling of the 3D ocean environment.
In 3D underwater networks, sensor nodes ﬂoat at different depths to observe a phenomenon.
In this architecture, each sensor is anchored to the ocean bottom and equipped with a ﬂoating buoy that can be inﬂated by a pump
The buoy pushes the sensor toward the ocean surface.
The depth of the sensor can then be regulated by adjusting the length of the wire that connects the sensor to the anchor by means of an electronically controlled engine that resides on the sensor.
AUVs can function without tethers, cables, or remote control, and therefore they have a multitude of applications in oceanography, environmental monitoring, and underwater resource studies.

## Slide 35: Wireless Underground Sensor Networks
Application areas of WUSN
  Agriculture: Soil conditions monitor, Automatic sprinkler system
  Security: To detect movement via pressure, vibration, or sound. May be used in business, home security, military
  Infrastructure monitoring: To monitor and detect leakage in electrical / communication wiring, plumbing